## Slide 1
Higher Energy State Classification of IBM Quantum Computer using Machine Learning
I-Tung Chen, Department of Electrical and Computer Engineering, University of Washington.
, where
1
0
and
1. Quantum Computer Introduction:
Qubits
0
1
or
Classical bits
Superposition
Entanglement(Spooky interaction)
1
0
0
1
or
Requirements for Qubits
1
0
Two level system
Indistinguishable
0
1
0
2. QC Access with IBM Quantum (Qiskit)
ibmq_Armonk
Qubit number: 1
Readout error: 2.77e-2
Anharmonicity: -0.34719GHz
Abstract: The higher energy state can be potentially used in quantum information processing but to correctly classify different energy state within a qubit is still challenging. This work try to explore the higher energy state and build a classifier to optimize the classification task.
3. Qubit Caliberation
|0> ->|1> State Calibration
|1> ->|2> State Calibration
Center frequency: 4.9717GHz
Pi Amplitude: 0.1414GHz
Score: 0.963
4. Higher Energy State and Classification
|1> ->|2> Discrimination
Sideband frequency: 4.6235GHz
Score: 0.808
LDA
Score: 0.840
MLP
Score: 0.841
Hidden layer neurons: 100